## Slide 1
Bufford Furman
Ron Swenson
Eric Rosenfeld
Solar Installation for an Automated Transit Network Podcar City, Antwerp – September 21, 2016

## Slide 2: Presentation Overview
Introduction
Overall Progress
Next steps
Objectives

## Slide 3: Hitting five birds with one stone
Energy Users
Energy Sources

## Slide 4: Power Estimation- Full Scale
Must know location and constraints
of the Spartan Superway transit system.

## Slide 5: Pod capacity will be traffic dependent
Chart: Hours
Number of cars assumed: 88
RMS = 44 rides
Notes: A recent study on ATN for the city of San José done by the Aerospace Corporation found that congestion on the network would occur if the maximum number of slots occupied by ATN vehicles exceeded about 70% of the total number of slots (Paige, 2012)

## Slide 6: How to account for power consumption?
Air resistance
Rolling resistance
Auxiliary power
Deceleration losses
2Anderson, J. E. (1988). What determines transit energy use? Journal of Advanced Transportation ATR, 22(2), 108-132. doi:10.1002/atr.5670220203
Notes: Show pictures of trains vs pod system. **

## Slide 7: Overall Pod Car Losses
Drag Force Losses= 5.09 kW/car
Cd=0.65
Rolling Resistance Losses= 1.00 kW/car
Overall pod consumption due to loss variable losses is 13.49 kW per car
Notes: Find out which wind speed was input to solidwork wind simulation.

## Slide 8: Energy Estimation
Energy | 28,490.20 | kWh | per day
 | 10,403,242 | kWh | per year
Variable | Value | Unit
Gravitational acceleration | 9.81 | m/s2
Auxiliary power |  | kW
Time | 293 | s
Efficiency of the motor Number of vehicles Mass (vehicle) Operating speed Air density Coefficient of air drag Wind speed Average distance between stops Maximum acceleration Rolling resistance coefficients C1 C2 Change in elevation | 0.85 150 1900 13.4 1.225 0.51 9 3500 4 0.0095 0.0004935 10 | % - kg m/s kg/m3 - m/s m m/s2 N/kg kg.m/s m
Variable | Value | Unit
Gravitational acceleration | 9.81 | m/s2
Auxiliary power |  | kW
Time | 293 | s
Efficiency of the motor Number of vehicles Mass (vehicle) Operating speed Air density Coefficient of air drag Wind speed Average distance between stops Maximum acceleration Rolling resistance coefficients C1 C2 Change in elevation | 0.85 150 1900 13.4 1.225 0.51 9 3500 4 0.0095 0.0004935 10 | % - kg m/s kg/m3 - m/s m m/s2 N/kg kg.m/s m

## Slide 9: Finally we know the yearly consumption!
Yearly Production
How many solar panels do we need?
Yearly Consumption
10.4 mi kWh
Number of modules: 19,600
  Required area: 38,300 m2
Flex-02 350W | Symbol | Performance
Nominal Power | W | 360.192
Efficiency | % | 18.4147
Maximum Power Current | A | 9.4
Open Circuit Voltage | V | 46.9
Area | m2 | 1.956
Weight | Kg | 19.3
The SunEdison SE-R360EzC-4y is assumed.

## Slide 10: A grid system will be utilized!
Notes: Simplify grid with circles

## Slide 11
The racking system is designed for automated
installation.

## Slide 12
The Racking System will utilize that frame of the Spartan Superway.
Notes: No slide

## Slide 13: Blind-connecting maximizer for each panel
Maximizer
Connectors
Wire
Copper Pieces

## Slide 14: Why consider a higher installed capacity?
More leftover energy
Payback Period
Notes: Renewable Energy Finance Tracking Initiative (REFTI) by National Renewable Energy Laboratory

## Slide 15: What is next?
Improve pod car design
Implement a full scale test track
Financial Analysis
Design a racking system for the Solar PV

## Slide 16
Questions?