## Slide 1: Bogie Design for a Suspended Solar-Powered ATN Vehicle
Mohammed Saiyed
Department of Mechanical Engineering
San Jose State University
May 14th, 2020

## Slide 2: Automobiles are a huge part of American Culture.
A typical “American Dream” involves a family, a house and a shiny car in the driveway

## Slide 3: Major problems that are created by the automobile industry
Traffic
Air Pollution
Fuel Dependency

## Slide 4: State of Public Transportation in Big Cities
San Jose
San Francisco
Requires more land & adds to the street traffic
Requires expensive tunnel system to operate under ground

## Slide 5: SPARTAN Superway solves most transportation problems by using Solar Power to operate & rising above the street level
Solar
Powered
Automated
Rapid
Transit
Ascendant
Network

## Slide 6: SPARTAN Superway provides an uninterrupted travel from origin to destination with the use of offline stations.
Offline Stations
Solidworks model of SPARTAN Superway track designed by 2014-2015 students showing offline stations on a guideway

## Slide 7
Design a bogie for Spartan Superway from which a passenger cabin is suspended below, which will allow the bogie to take one path or the other at a junction on the guideway

## Slide 8: Suspended monorails that are already in service.
H-Bahn Bogie Frame
H-Bahn Cabin Suspended From the Bogie

## Slide 9: Designing a bogie system that can maneuver a passive guideway with junctions without derailing
Isometric view of guideway junction
Bottom view of guideway junction
One wheel will be hanging during the turns
Bogie wheels rests on highlighted surface
Working in conjunction with Liwei Lu

## Slide 10: Different switching mechanism used commercially and previous work done by SPARTAN Superway.
H-Ban switching mechanism
Bill’s design (SPARTAN Superway), 2020

## Slide 11: Design Overview for Bogie Assembly showing major components
Switching Mechanism
Switch support
Frame Shock Mount
Swingarm
Drive Wheels
Guide Wheels
Cabin is Attached Here
Battery Pack
Bogie Frame

## Slide 12: Bogie on top of a guideway with switching mechanism in action
Bottom guide wheels making contact with the track to keep the bogie centered on the track
Switch hooks theses wheels into the track to turn the bogie

## Slide 13: Switch bar support to compliment the switching mechanism
Transfers load to the frame
Direction of Load
Rubber to reduce noise

## Slide 14: FEA analysis results of the support block to transfer load to the frame.
Factor of Safety (minimum = 5.3)
Deflection (maximum = 0.0022mm)
Von Mises (maximum 5.1E6Pa)

## Slide 15: Frame components
Cabin Attached Here
Forks for guidewheels
Weight Saving cutouts
Attached using L brackets and bolts
Follows the curve to transfer load to the frame

## Slide 16: FEA analysis results for the bogie frame and frame shock mount
10000N
2500N
Maximum Stress 1.17E8 Pa
Minimum Factor of Safety 5.3
Maximum Deflection 0.40mm
Maximum Stress 8.03E7 Pa
Minimum Factor of Safety 4.3
Maximum Deflection 0.32mm

## Slide 17: Swingarm design ang how it works with the frame
Swing Arm Pivot Points
Shock Mount
Adjustable Axle

## Slide 18: Swingarm FEA analysis results
2500N
Fixed
Factor of Safety (minimum = 2.1)
Deflection (maximum = 0.86mm)
Von Mises (maximum 2.8E8Pa)

## Slide 19: Battery pack specifications
High Voltage Pack | 
Parallel Connections | 16
Series Connections | 72
Total Cells | 1152 Cells
Voltage | 273.6 V
Capacity | 21,888 Wh
Cell Weight | 74.88 Kg
Low Voltage Pack | 
Parallel Connections | 32
Series Connections | 36
Total Cells | 1152 Cells
Voltage | 136.8 V
Capacity | 21,888 Wh
Cell Weight | 74.88 Kg

## Slide 20: Battery pack assembly showing all major components.
End copper plates
LHS ABS Side Plate
RHS ABS Side Plate
Cross brace
Terminal Busbar
1/16” G10 Sheet
Copper Plates
Local Busbar
G10 Terminal cover

## Slide 21: Using pulse spot welding to weld the cells to the copper plates
Press in and spot weld
Pulse Spot Welder

## Slide 22: FEA analysis results for horizontal switch bar
50N
Fixed
Factor of Safety (minimum = 13)
Deflection (maximum = 0.92mm)
Von Mises (maximum 4.5E7Pa)

## Slide 23: Improved switching mechanism design
Using I Beams instead of U
Using two Separate bars instead of one

## Slide 24: Relationship between wheel diameter and RPM at constant velocity of 25mph.
Wheel Diameter | RPM
8” = 0.2032m | 1050
10” = 0.254m | 840
12” = 0.3048m | 700
Chart: Wheel Diameter Vs. RPM
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
 | 2100 | 1680 | 1400 | 1200 | 1050 | 934 | 840 | 764 | 700 | 646 | 600 | 560 | 525

## Slide 25: Future Work: Using ANSYS to optimize dimensions for the parts that are custom.
This can reduce the maximum stress and the weight of the part at the same time. Mostly used to calculate dimensions of weight reduction holes in part.

## Slide 26: Future Work: Finding a shock absorber and a hub motor that works with the system.
Might have to change the swingarm to accommodate longer shock absorber.

## Slide 27: Future Work: Introduce water cooling to the 21700 battery pack
2D CFD analysis using ANSYS Fluent
Tesla Model S Battery Module
Thermal Management System
Temperature contour of 2D CFD analysis of water cooling battery cells
Inlet
Outlet

## Slide 28: Future Work: Building a prototype
Frame uses standard dimension tubing, which are easy to find off the shelf, and weld them together.

## Slide 29: ACKNOWLEGEMENTS
Burford Furman
Ron Swenson
James Mokri
Liwei Lu
Eric Hagstorm
Dan Espinosa